## Slide 1: CTP Communication Protocol
22 Feb, 2011
zhongxy

## Slide 2: Contents
CTPM Interface
IIC Standard Protocol
  Coordinate Data Read
  Register read/write
FTS 26 Bytes(IIC/SPI) Protocol
  Coordinate Data Read
  Register read/write
Update CTPM Firmware
Notes: 本Slide的时间??
讲授顺序??
采用例子??
其它技巧??

## Slide 3: CTPM Interface
Figure 1-1 shows how CTPM communicates with the Host，there are two ways communicate between CTPM and Host，we will introduce each communication in this section.
  1、BUS: Transfer the data via I2C/SPI;
  2、/INT: Send interrupt once there is a valid touch;
  3、/WAKE: Host send Wakeup signal to CTPM;

## Slide 4: CTPM Interface
4、Power Supply voltage： 2.8V~3.3V,
5、interface voltage：2.8V~3.3V.
For the detail, please refer to Table 1-1.
NOTE: FT5x06 serial interface ：2.8V~3.3V or 1.8V

## Slide 5: IIC Standard Potocol
I2C Read/Write Interface description
Host write data to slave
Host read data from slave
step1:write data address
step2:read data
Notes: 本Slide的时间??
讲授顺序??
采用例子??
其它技巧??

## Slide 6: IIC Standard Potocol
Coordinate Data Read
timing to get touch data

## Slide 7: IIC Standard Potocol
2.Coordinate data register map

## Slide 8: IIC Standard Potocol
GEST_ID

## Slide 9: IIC Standard Potocol
TD_STATUS（TOUCH EVENT）

## Slide 10: IIC Standard Potocol
3.Operating
Start | Slave Address | W | 0x01 | Stop
Start | Slave Address | R | (6*PointNum+2) Bytes | Stop

## Slide 11: IIC Standard Potocol
Register Read/Write
1.Used Register
Address | Bit Address | Register Name | Description
0x88 | 7：0 | ID_G_ PERIOD | Range form 3to14,default 6
0xa5 | 7：0 | ID_G_ PMODE | 0: active 1: monitor 3: hibernate(deep sleep)
0xa6 | 7：0 | ID_G_ FIRMWARE_ID | R: xx
0xa1 | 7：0 | ID_G_LIB_VERSION_H | R: xx
0xa2 | 7：0 | ID_G_ LIB_VERSION_L | R: xx

## Slide 12: IIC Standard Potocol
2.Operating
a)Register Write
Start | Slave Address | W | Register Address | Data | Stop
b)Register Read
Start | Slave Address | W | Register Address | Stop
Start | Slave Address | R | 1 Byte | Stop

## Slide 13: IIC Standard Potocol
Read Raw Data
  Start scanning: write register 0x00 to 0xc0
  Wait for scanning complete: read register 0x00
  Write LineNum to register 0x01 then read data
Start | Slave Address | W | 0x00 | 0xc0 | Stop
Start | Slave Address | W | 0x00 | Stop
Start | Slave Address | W | 0x01 | Line Num | Stop
Start | Slave Address | W | 0x10 | Stop
Start | Slave Address | R | (2*RxNum) Bytes | Stop
Start | Slave Address | R | 1 Byte | Stop

## Slide 14: FTS 26 Bytes(IIC/SPI)
Coordinate Data Read
timing to get touch data

## Slide 15: FTS 26 Bytes(IIC/SPI)
2.Coordinate data register map
 | Packet Head | Packet Length | Point Num | Gesture Code | X1 | Y1 | X2 | Y2 | X3 | Y3 | X4 | Y4 | X5 | Y5 | Check Code
Bytes | 2 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 |  | 1
Data | 0xAAAA | 0x1A |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 16: FTS 26 Bytes(IIC/SPI)
GEST_ID

## Slide 17: FTS 26 Bytes(IIC/SPI)
TD_STATUS（TOUCH EVENT）

## Slide 18: FTS 26 Bytes(IIC/SPI)
3.Operating
Start | Slave Address | W | 0xF9 | Stop
Start | Slave Address | R | 26 Bytes | Stop

## Slide 19: FTS 26 Bytes(IIC/SPI)
Register Read/Write
1.Used Register
Address | Bit Address | Register Name | Description
0x08 | 7：0 | ID_G_ PERIOD | Range form 3to14,default 6
0x3a | 7：0 | ID_G_ PMODE | 0: active 1: monitor 3: hibernate(deep sleep)
0x3b | 7：0 | ID_G_ FIRMWARE_ID | R: xx
0x36 | 7：0 | ID_G_LIB_VERSION_H | R: xx
0x37 | 7：0 | ID_G_ LIB_VERSION_L | R: xx

## Slide 20: FTS 26 Bytes(IIC/SPI)
2.Operating
a)Register Write
b)Register Read
Start | Slave Address | W | 0xFC | Register Address | Data | Checksum | Stop
Start | Slave Address | W | 0xFC | Register Address+0x40 | Stop
Start | Slave Address | R | 2 Bytes | Stop

## Slide 21: FTS 26 Bytes(IIC/SPI)
Read Raw Data
  Start scanning write register 0x08 to 0x01
  Wait for scanning complete: read register 0x08
  Write LineNum to register 0x0c then read data
Start | Slave Address | W | 0xF3 | 0x08 | 0x01 | checksum | Stop
Start | Slave Address | W | 0xF3 | 0x08+0x80 | Stop
Start | Slave Address | R | 2 Bytes | Stop
Start | Slave Address | W | 0xF5 | 0x0C | LineNum | Stop
Start | Slave Address | R | (2*RxNum)+1 Bytes | Stop
Notes: Checksum = 0xF3^0x08^0x01

## Slide 22: Update TP Firmware
FT5x06 upgrade
(Flash layout)
Setting frame structure: |  |  |  |  |  |  |  |  | 
0x6ffa | 0x6ffb | 0x6ffc | 0x6ffd | 0x6ffe | 0x6fff | 0x7800 | 0x7801 | 0x7802 | 0x7803
F/W Length |  | F/W Length negate |  | ECC | ECC negate | Slave_ address | Slave_ address negate | I/O voltage | I/O voltage negate
ECC: shows F/W all data Xor checksum I/O voltage: 0x00=3.3V; 0x01=1.8V |  |  |  |  |  |  |  |  | 
Upgrade (1924Bytes) | 0K
Public (124Bytes) | 
App_1(26624Bytes) | 2K
App_0 (2048Bytes) | 28K
Setting | 30K 31K

## Slide 23: Update TP Firmware
CTPM upgrade flowchart:
Power On/Reset
FW self check
Correct ?
Start 30ms counting
Receive
0x55, 0xaa
Normal Start
Start Upgrade
N
Correct ?
Time up ?
Spend about 20ms
Y
Y
Y
N
N

## Slide 24: Update TP Firmware
Host upgrade
Flowchart:
Start
Reset CTPM, delay 30ms
Send data packet, delay N*50us
Erase, delay 1s
Finish
N
ID correct ?
Y
Y
Y
N
N
Send 0x55,
delay 10us
Send 0xaa,
delay 10us
Check ID
A
A
Finish ?
Read ECC
ECC correct ?
Upgrade success & reset
Upgrade fail

## Slide 25: Update TP Firmware
Start the Upgrade: Power or Reset
1.Power on to start upgrade timing:
2.Reset to start upgrade timing:

## Slide 26: Update TP Firmware
3.I2C timing

## Slide 27: Update TP Firmware
Example Code
E_UPGRADE_ERR_TYPE fts_ctpm_fw_upgrade(FTS_BYTE* pbt_buf, FTS_DWRD dw_lenth)
{
FTS_BYTE cmd_len = 0;
FTS_BYTE reg_val[2] = {0};
FTS_DWRD i = 0;
FTS_BYTE ecc = 0;
FTS_DWRD packet_number;
FTS_DWRD j;
FTS_DWRD temp;
FTS_DWRD lenght;
FTS_BYTE packet_buf[FTS_PACKET_LENGTH + 6];
FTS_BYTE auc_i2c_write_buf[10];
FTS_BYTE bt_ecc;
/*********Step 1:Reset CTPM *****/
/*write 0xaa to register 0xfc*/
fts_register_write(0xfc,0xaa);
delay_ms(50);
/*write 0x55 to register 0xfc*/
fts_register_write(0xfc,0x55);
printk("Step 1: Reset CTPM test\n");
delay_ms(40);

## Slide 28: Update TP Firmware
/*********Step 2:Enter upgrade mode *****/
auc_i2c_write_buf[0] = 0x55;
auc_i2c_write_buf[1] = 0xaa;
i2c_write_interface(I2C_CTPM_ADDRESS, auc_i2c_write_buf, 2);
printk("Step 2: Enter update mode. \n");
/*********Step 3:check READ-ID***********************/
/*send the opration head*/
do{
if(i > 3)
{
return ERR_READID;
}
/*read out the CTPM ID*/
cmd_write(0x90,0x00,0x00,0x00,4);
byte_read(reg_val,2);
i++;
printk("Step 3: CTPM ID,ID1 = 0x%x,ID2 = 0x%x\n",reg_val[0],reg_val[1]);
}while(reg_val[0] != 0x79 || reg_val[1] != 0x03);

## Slide 29: Update TP Firmware
/*********Step 4:erase app*******************************/
cmd_write(0x61,0x00,0x00,0x00,1);
delay_ms(1500);
printk("Step 4: erase. \n");
/*********Step 5:write firmware(FW) to ctpm flash*********/
bt_ecc = 0;
printk("Step 5: start upgrade. \n");
dw_lenth = dw_lenth - 8;
packet_number = (dw_lenth) / FTS_PACKET_LENGTH;
packet_buf[0] = 0xbf;
packet_buf[1] = 0x00;
for (j=0;j<packet_number;j++)
{
temp = j * FTS_PACKET_LENGTH;
packet_buf[2] = (FTS_BYTE)(temp>>8);
packet_buf[3] = (FTS_BYTE)temp;
lenght = FTS_PACKET_LENGTH;
packet_buf[4] = (FTS_BYTE)(lenght>>8);
packet_buf[5] = (FTS_BYTE)lenght;

## Slide 30: Update TP Firmware
for (i=0;i<FTS_PACKET_LENGTH;i++)
{
packet_buf[6+i] = pbt_buf[j*FTS_PACKET_LENGTH + i];
bt_ecc ^= packet_buf[6+i];
}
byte_write(&packet_buf[0],FTS_PACKET_LENGTH + 6);
delay_ms(FTS_PACKET_LENGTH/6 + 1);
if ((j * FTS_PACKET_LENGTH % 1024) == 0)
{
printk("upgrade the 0x%x th byte.\n", ((unsigned int)j) * FTS_PACKET_LENGTH);
}
}
if ((dw_lenth) % FTS_PACKET_LENGTH > 0)
{
temp = packet_number * FTS_PACKET_LENGTH;
packet_buf[2] = (FTS_BYTE)(temp>>8);
packet_buf[3] = (FTS_BYTE)temp;
temp = (dw_lenth) % FTS_PACKET_LENGTH;
packet_buf[4] = (FTS_BYTE)(temp>>8);
packet_buf[5] = (FTS_BYTE)temp;
for (i=0;i<temp;i++)
{
packet_buf[6+i] = pbt_buf[ packet_number*FTS_PACKET_LENGTH + i];
bt_ecc ^= packet_buf[6+i];
}
byte_write(&packet_buf[0],temp+6);
delay_ms(20);
}

## Slide 31: Update TP Firmware
//send the last six byte
for (i = 0; i<6; i++)
{
temp = 0x6ffa + i;
packet_buf[2] = (FTS_BYTE)(temp>>8);
packet_buf[3] = (FTS_BYTE)temp;
temp =1;
packet_buf[4] = (FTS_BYTE)(temp>>8);
packet_buf[5] = (FTS_BYTE)temp;
packet_buf[6] = pbt_buf[ dw_lenth + i];
bt_ecc ^= packet_buf[6];
byte_write(&packet_buf[0],7);
delay_ms(20);
}
/*********Step 6: read out checksum***********************/
/*send the opration head*/
cmd_write(0xcc,0x00,0x00,0x00,1);
byte_read(&reg_val,1);
printk("Step 6: ecc read 0x%x, new firmware 0x%x. \n", reg_val[0], bt_ecc);
if(reg_val[0] != bt_ecc)
{
return ERR_ECC;
}
/*********Step 7: reset the new FW***********************/
cmd_write(0x07,0x00,0x00,0x00,1);
return ERR_OK;
}

## Slide 32
Thank you !!